TRAFFIC AND SAFETY INFORMATIONAL SERIES

FREQUENTLY ASKED QUESTION #8

WHY ISN'T THERE A “SCHOOL BUS STOP AHEAD” SIGN EVERYWHERE A BUS STOPS?

Signs improve the safety of a roadway by warning of hazards and assisting with the orderly and predictable movement of traffic. Before a sign can be placed along a roadway it must meet four requirements:

- The sign should fulfill a need. This need should be identified by a field study or from previous traffic incidents.

- The sign should draw attention. The purpose of a sign is defeated if roadway users do not notice it.

- The sign should have a clear message that all roadway users can understand.

- The sign should be placed properly so that the users of the road have enough time to respond to its message.

The specific location, number, and characteristics of signs placed within a roadway right-of-way must meet the requirements of the Manual on Uniform Traffic Control Devices (MUTCD). In addition, the placement of a sign within the right-of- way of a roadway must be authorized by the jurisdiction that owns and/or maintains the roadway.

THE “SCHOOL BUS STOP AHEAD” SIGN

According to the MUTCD, a “School Bus Stop Ahead” sign (see Figure 1) is warranted if the visibility or roadway sight distance to the bus stop area is 500 feet or less. Whether this requirement is met at a particular bus stop location is determined by an engineering study of the roadway terrain. If the sight distance is inadequate, an alternate bus stop location should be considered (for safety reasons) before a “School Bus Stop Ahead” sign is installed. If the terrain or roadway features do not allow an alternative bus stop location, a “School Bus Stop Ahead” sign should be installed at bus stop locations with restricted sight distance. Typically, a specific school bus stop location is investigated if a request is filed with the government entity that has signing authority along that particular roadway. The placement of unnecessary “School Bus Stop Ahead” signs reduces the overall effectiveness of these signs.

FIGURE 1  “School Bus Stop Ahead” sign.

Reference: Manual on Uniform Traffic Control Devices.

OVERUSE OF A “SCHOOL BUS STOP AHEAD” SIGN

The purpose of a “School Bus Stop Ahead” sign is to warn drivers of unexpected hazards (e.g., a bus stopped in the roadway and/or crossing passengers). If these signs were placed at every bus stop location, even where the bus (with flashing lights) and passengers are visible from an adequate distance, the “School Bus Stop Ahead” sign would become ineffective. This phenomenon would occur even where these signs were really needed (i.e., where the driver cannot see the stopped school bus).  Drivers would begin to believe that if they can’t see a bus at locations with a “School Bus Stop Ahead” sign that there is no bus there (over the hill or around the curve), and no reason for caution.  This reaction is caused by the overuse and misuse of “School Bus Stop Ahead” signs, and can have serious consequences.  The consistent and prudent use of these types of signs is needed to ensure their effectiveness.  If a driver begins to see these signs at a large number of locations (where they are not needed) they may begin to ignore them completely.

For more information

For more information, please contact 							.