TRAFFIC AND SAFETY INFORMATIONAL SERIES

FREQUENTLY ASKED QUESTION #2

how MANY BULLET HOLES DOES IT TAKE TO KILL A SIGN?

(SIGN vANDALISM)

Sign vandalism is a serious problem in Iowa. In fact, it is believed that one of ten signs is vandalized each year. As expected, roadways with low traffic volume account for about 80 percent of the signs vandalized each year. Overall, the cost of sign vandalism each year in the United States is about $274,100,000. There have been a number of steps taken to reduce the amount of sign vandalism, but no single action has worked completely.

Signs are important: they regulate the actions of drivers, warn drivers of hazards, and inform drivers of important locations. Signs are placed and/or designed to fulfill a need, command attention and respect, convey a clear and legible message, and provide drivers with enough time to respond correctly. A sign damaged by vandalism can not perform any of these functions effectively. Although the sign is still needed, when it is damaged it may not command attention and respect, or convey a clear and legible message. The vandalism or removal  (another form of vandalism) of a sign can have serious consequences.

Types of sign Vandalism

There are many kinds of sign vandalism. While some people believe that shooting signs (see Figure 1) is the most common, a study by the Iowa Department of Transportation found that only about 11 percent of vandalized signs are shot by a gun.  Broken/knocked down signs and stolen signs ranked first and second, respectively, and gun-damaged signs third. Other kinds of vandalism include painting or marring the face of a sign, pulling out a sign, and bending a sign. All of these can produce serious safety problems and should be mitigated as soon as possible.

FIGURE 1  Sign vandalized by gun.

Factors for Replacing or Fixing Vandalized Signs

Vandalized signs provide a poor impression of the surrounding community. Studies have shown that not replacing or fixing vandalized signs can lead to more severe vandalism. Vandalized signs should be repaired or replaced as soon as possible.

replacement of Vandalized Signs

A vandalized sign may no longer be effective and can be hazardous to road users. Motorists could be deprived of critical information, and this could result in a collision. Critical signs include “Stop” signs, “Yield” signs, and “Do Not Enter” signs. Warning signs caution motorists of potential danger. If a warning sign is missing or unreadable it may also lead to a collision. Warning signs include signs that alert motorists of approaching intersections, curves, turns, and stop signs or signals. Finally, there are guide signs. These signs guide motorist to points of interest and make trips less confusing. Guide signs are important because they produce a less confusing environment and allow the driver’s attention to be directed toward the roadway.

Countermeasures for Sign Vandalism

For a description of techniques to combat sign vandalism, consult the Manual on Countermeasures for Sign Vandalism (US Department of Transportation, Federal Highway Administration).

For more information

For more information, please contact 							.